## Slide 1: CHAPTER SEVEN
SOUND

## Slide 2: DIGITAL SOUND
Two major types of digital sound:
  Sampled sound: digital recording of previously existing analog sound wave.
    File contains numeric values to describe the amplitude of the sound wave at a particular instant.
    Used to capture and edit naturally-occurring sounds.
  Synthesized sound: new sound generated by the computer.
    File contains instructions the computer uses to reproduce the sound.
    Used to:
      Create original compositions
      Produce novel sound effects.

## Slide 3: SAMPLED SOUND
Analog to Digital Converter captures separate measures of sound amplitude.
  Samples are recorded as digital numbers.
Digital values are used to recreate the analog form using a Digital to Analog Converter.
Quality of the sampling depends on:
  Sample resolution
  Sample rate.

## Slide 4: SAMPLE RESOLUTION
Number of bits to encode amplitude.
  Sample resolutions range from 8-bit to 24-bit.
8-bit resolution captures 256 different amplitude levels.
  Adequate for limited decibel range.
16-bit CD quality sound has 65,000 different levels.
24-bit DVD audio can generate over 16 million different levels.

## Slide 5: SAMPLE RATE
Number of samples taken in a fixed interval of time.
  Stated in thousands of Hertz, or kilohertz.
  Determines the range of frequencies that can be represented in a digital recording.
Two measurements capture each cycle of the sound wave:
    High value or peak
    Low value or trough.
  CD-quality sound captures 44.1kHz to record frequencies as high as 22.05kHz.
Highest frequency the human ear can detect is 20kHz.

## Slide 6: SOUND COMPRESSION
Compression is best strategy to lower file size for sounds with wide range of frequencies and amplitudes.
Lossy codecs use various techniques to reduce sound file sizes.
  Psychoacoustics: eliminates frequencies indistinguishable to the human ear.
  Variable bitrate encoding (VBR): alters the number of bits to encode the sample depending on the complexity of the sound.
Notes: Compression strategies are both lossless and lossy. Have students comment on why lossless strategy is not used in sound, but is critical for text compression.

## Slide 7: SYNTHESIZED SOUND
Computer sends commands to specialized electronic device called a synthesizer.
MIDI (Musical Instrument Digital Interface).
  Most common standard to code commands for synthesizers.
  Codes provided for:
    Specific instruments
    Notes
    Force and duration of note
    Routing commands to different instrument channels
    Specialized control functions.

## Slide 8: DELIVERING DIGITAL SOUNDS
Downloaded audio transfers the complete audio file from the server to the client.
  File remains on client computer for replay and editing.
Progressive downloads: file is saved to client computer, but begins to play from RAM as it is downloading.
Streaming audio: real-time sound that is played as it is being delivered. Not saved on client computer.
  Requires special protocols, special servers, special media formats and players.
Notes: Discuss benefits and drawbacks of each technique. Note particularly the copyright issues with each. Have students identify methods used by iTunes, a live concern of a band, a song shared on peer to peer networking.